## Slide 1: Effect of Stator Cooling Channel Position on Thermal Performance of Oil-Cooled Motor
Chengyang Ye, Andrea Tonoli*, Enrico Cesare Zenerino
Politecnico di Torino

## Slide 2: Motivations and objectives
Motivation
Cooling is a key issue in electric traction motors to improve the power density and efficiency
Main cooling types are:
Water jacket
Direct cooling by means of
-Spray cooling of end windings
-Liquid cooling of end windings
-Liquid cooling of end windings and slots (most efficient)
Considering slot liquid cooling, the best position of the cooling channel is not investigated yet especially in case of hairpin windings with high filling factors.
Objective
Investigate the cooling performance of different radial positions of the cooling channel in stator cooling systems with hairpin windings.

## Slide 3: Study case: EESM motor
Main characteristics:
Stator Outer Diameter: 175.14 mm
Stator inner Diameter: 116.62 mm
Motor length: 105 mm
Slot number : 48
Oil flow rate: 10 L/min
The winding is a hairpin.
Peak power: 36 kW
Peak torque: 80 Nm
Application:
Electrically excited synchronous motor for automotive traction.

## Slide 4: Stator cooling strategies
a)
b)
c)
Slot
Outlet
Inlet
lamination slot cooling (reference)
winding outer slot cooling
winding inner slot cooling
Cooling channel

## Slide 5: winding coordinate and boundary condition
slot winding
x
y
z
y
x
z
end winding
Only one slot is included in the CFD model
The interface between each area is considered as a symmetric boundary condition
Losses are considered as a homogeneous heat source

## Slide 6: Equivalent winding
y
z
x
Equivalent winding
a)
b)
Side insulation modeled as thermal resistance
Z-direction:
Copper and insulation in series Equivalent conductivity based on relative thickness → Inverse rule of mixtures
y-direction:
Copper and insulation first in parallel Equivalent conductivity based on relative thickness → Rule of mixtures Side insulation → additional thermal resistance
x-direction:
Copper and insulation in parallel Equivalent conductivity based on filling factor → Rule of mixtures

## Slide 7: Loss model and working point
The loss is considered as temperature depended
Copper loss
Iron loss
Working point :
5000 rpm
35 Nm
Copper loss : 1390
Iron loss: 292
Flow rate: 10L/min

## Slide 8: Results
a)
b)
c)
Winding temperature
a)
b)
c)
Stream line
Better cooling on end winding

## Slide 9: Results: temperatures in cross section
Temperature [℃]
a)
b)
c)
Temperature in the middle cross-section

## Slide 10: Sensitivity analysis
copper loss equal to 500 W
The advantage between the winding inner/outer cooling is decided by the ratio of copper and iron loss
iron loss equal to 300 W
breakeven
Inner slot cooling leads to higher temperatures with increasing iron losses.
Outer slot cooling leads to higher temperatures with increasing copper loss

## Slide 11: Conclusions
The winding can be modeled as an equivalent entity to reduce computational cost.
The radial cooling channel configurations show the following characteristics:
Lamination-slot cooling:
+ Easy to manufacture
- Relatively limited cooling performance
Winding outer-slot cooling
+ Better cooling of iron losses
- Less effective cooling of copper losses.
Winding inner-slot cooling
+ Better cooling of copper losses
- Less effective cooling of iron losses.

## Slide 12: Thank you
Andrea.tonoli@polito.it